2D detection
Resnet 50

---
mask_rcnn_r50_fpn.py
1. Backbone
  - Resnet
  - Depth = 50
  - Num_stages = 4 (by default)
  - Out_indices (indices for each stage)
  - frozen_stages = 1
  - norm_cfg = BN (Batch normalization)
- 2. Neck
  - In channel = [256,512,1024,2048]
  - out_channel = 256
  - num_outs = 5
- 3. RPN_head
  - In channel = 256
  - Feature channels = 256
  - Anchor generator
  - BBOX coder
  - Loss classification: Cross entrpy
  - Loss bbox = L1 loss
- 4. ROI head
  - Bbox roi extractor
    - Roi layer = roi_align, output size = 7
    - out_channel = 256
  - Bbox head
    - in_channel = 256
    - fc_out_channel = 1024
    - roi_feat_size = 7
    - num_class = 10
    - Loss classification: Cross entrpy
    - Loss bbox = L1 loss
STAGES OF RESNET50 FPN (feature pyramid network)
Stem: P1
7
×
7
7×7 convolution and
3
×
3
3×3 max pooling.
Stage 1: P2
3 residual blocks with feature map size
56
×
56
56×56 (for an input image of
224
×
224
224×224).
Stage 2: P3
4 residual blocks with feature map size
28
×
28
28×28.
Stage 3: P4
6 residual blocks with feature map size
14
×
14
14×14.
Stage 4:
3 residual blocks with feature map size
7
×
7
7×7.
This gives a total of 4 stages.
Typical RESNET block
Input -> Conv -> BN -> ReLU -> Conv -> BN -> Add (Residual) -> ReLU
Example neck
Input -> Conv(1x1) -> BN -> ReLU -> Conv(3x3) -> BN -> ReLU -> Conv(1x1) -> BN -> Add (Residual) -> ReLU

---
Single_frame.py
- Decide on the dimension of the ROI.
  - ida_aug_conf = {
  - "resize_lim": (0.8, 1.0), //1.0,1.0
  - "final_dim": (512, 1408), //dim of ROI
  - "bot_pct_lim": (0.0, 0.0),
  - "rot_lim": (0.0, 0.0),
  - "H": 900, //1024
  - "W": 1600, //1024
  - "rand_flip": True,
  - }
Change class_names

---
mv2d_r50_single_frame_roi_1408x512.py
- Point_cloud_range = given in meters. Need to change to actual dimensions for the data.
- post_range = same as above
- roi_size = 7 Roi_align resizes each selected region to 7x7 (default from resnet)
- roi_stride = downsampling factor between original image and the feature map = 16 (nuscenes)
  - This roi_stride needs to be tuned for cancer data.
- One STEM + 4 stages in resnet
- DCN (deformable convolution networks at last stages of resnet)
- grid_mask configuration for training. Can be tuned for cancer data to remove generalisation?
- Neck:
  - Only uses the 3rd stage feature output. Based on cancer data this needs to be tuned.
- ROI head
  - ROI_stride = 16 (to be tuned)
  - 1024*1024→128*128(3rd stage)→ each roi will be 16x16 so we get a 8x8 feature map → downsampled to 7x7
  - Output channels = 512