MV2Dbased lifting
ENSAI

---
2D detection
Mask RCNN
Input images (I_v)
RPN
RoI Align
Bounding box (B_i_v = x_min, x_max, y_min, y_max)
Feature maps for each bounding box Ov = RoI-Align(Fv , Bv ),
0 ≤ v < N.
[Speaker Notes: Input images: Denoted as I over v cameras. Mask RCNN is the 2D object detector. It contains the RPN (Region proposal network). RPN is a neural network that generates regions of interest (RoIs) based on the identification of potential objects in the image. Each region of interest is the bounding box and each bounding box is classified. Inside Mask RCNN there is also the RoI-Align which extracts feature maps from the RoIs. In our case each bounding box corresponds to 7x7 RoI align feature map having 512 channels.]

---
mask_rcnn_r50_fpn.py
1. Backbone
  - Resnet
  - Depth = 50
  - Num_stages = 4 (by default)
  - Out_indices (indices for each stage)
  - frozen_stages = 1
  - norm_cfg = BN (Batch normalization)
- 2. Neck
  - In channel = [256,512,1024,2048]
  - out_channel = 256
  - num_outs = 5
- 3. RPN_head
  - In channel = 256
  - Feature channels = 256
  - Anchor generator
  - BBOX coder
  - Loss classification: Cross entrpy
  - Loss bbox = L1 loss
- 4. ROI head
  - Bbox roi extractor
    - Roi layer = roi_align, output size = 7
    - out_channel = 256
  - Bbox head
    - in_channel = 256
    - fc_out_channel = 1024
    - roi_feat_size = 7
    - num_class = 10
    - Loss classification: Cross entrpy
    - Loss bbox = L1 loss
STAGES OF RESNET50 FPN (feature pyramid network)
Stem: P1
7
×
7
7×7 convolution and
3
×
3
3×3 max pooling.
Stage 1: P2
3 residual blocks with feature map size
56
×
56
56×56 (for an input image of
224
×
224
224×224).
Stage 2: P3
4 residual blocks with feature map size
28
×
28
28×28.
Stage 3: P4
6 residual blocks with feature map size
14
×
14
14×14.
Stage 4:
3 residual blocks with feature map size
7
×
7
7×7.
This gives a total of 4 stages.
Typical RESNET block
Input -> Conv -> BN -> ReLU -> Conv -> BN -> Add (Residual) -> ReLU
Example neck
Input -> Conv(1x1) -> BN -> ReLU -> Conv(3x3) -> BN -> ReLU -> Conv(1x1) -> BN -> Add (Residual) -> ReLU

---
mv2d_r50_single_frame_roi_1408x512.py
- Point_cloud_range = given in meters. Need to change to actual dimensions for the data.
- post_range = same as above
- roi_size = 7 Roi_align resizes each selected region to 7x7 (default from resnet)
- roi_stride = downsampling factor between original image and the feature map = 16 (nuscenes)
  - This roi_stride needs to be tuned for cancer data.
- One STEM + 4 stages in resnet
- DCN (deformable convolution networks at last stages of resnet)
- grid_mask configuration for training. Can be tuned for cancer data to remove generalisation?
- Neck:
  - Only uses the 3rd stage feature output. Based on cancer data this needs to be tuned.
- ROI head
  - ROI_stride = 16 (to be tuned)
  - 1024*1024→128*128(3rd stage)→ each roi will be 16x16 so we get a 8x8 feature map → downsampled to 7x7
  - Output channels = 512

---
Positional Encoding
- Encode 3D positional information into 2D features to get 3D position aware features.
- Earlier used to generate high resolution images from low resolution, by encoding HR co-ordinates into LR features.
- Type of Implicit neural representation (INR). Maps co-ordinates to visual signal by MLP.
- Anchor points in 3D space are transformed to object queries by a MLP.
- These further interact with 3D position aware features to predict corresponding 3D objects.
- In MV2D the PE is split into 2 parts:
  - Camera frustum coordinate positional encoding
  - 3D coordinate positional encoding

---
PETR method

---
3D coordinate generator PETR
u
j
v
. . .
Discretize the camera frustum space into D planes
d_j = (j/(D-1) * (Zmax – Zmin) + Zmin)
Eg: Z is from -10m to +10m
[Speaker Notes: Each feature map represented as u x v, is projected onto the camera frustum space. The equation is as shown in the figure. The depth discretization value d_j is obtained using varying methods. One of the methods involves smaller resolution of the discretization closer to the camera and larger steps further away. This ensures the]

---
3D position embedding + Position aware features

---
MV2D - Camera frustum co-ord PE
Flat
1D conv
Avg Pool
Linear
ReLu
F_i_v (7x7x512)
K_i_v
Intermediate updated feature map
p_i_v
[Speaker Notes: query_generator.py def get_roi_feat(self, x, extra_feats=dict()): This step creates an intermediate set of feature maps where the camera intrinsic params are positionally encoded with the RoI feature maps, and we obtain the 3D camera frustum coordinate space. For each bounding box in an image the NN learns the representation of the object location. p_i_v is the co-ordinate space that is generated from the co-ordinate space of the intermediate updated feature maps.]

---
3D co-ordinate position embedding
Queries are generated as:
Pref is normalized as:
[Speaker Notes: def center2lidar(self, center_pred, intrinsic, extrinsic) reference_points, return_feats = self.query_generator(bbox_feats, intrinsics, extrinsics, extra_feats) reference_points[..., 0:1] = (reference_points[..., 0:1] - self.pc_range[0]) / ( self.pc_range[3] - self.pc_range[0]) reference_points[..., 1:2] = (reference_points[..., 1:2] - self.pc_range[1]) / ( self.pc_range[4] - self.pc_range[1]) reference_points[..., 2:3] = (reference_points[..., 2:3] - self.pc_range[2]) / ( self.pc_range[5] - self.pc_range[2]) reference_points.clamp(min=0, max=1) SinePositionalEncoding3D]